## Slide 1
Chapter 3 Transport Layer
Teacher: Xu Yang

## Slide 2: Chapter 3: Transport Layer
our goals:
understand principles behind transport layer services:
  multiplexing, demultiplexing
  reliable data transfer
  flow control
  congestion control
learn about Internet transport layer protocols:
  UDP: connectionless transport
  TCP: connection-oriented reliable transport
  TCP congestion control

## Slide 3: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control
Notes: providing communication services directly to the application processes running on different hosts.

## Slide 4: Transport Layer
Physical communication/connection: connection through physical medium/link
Logical communication/connection: the connection between two end system running the same protocol at the same layer
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
Ht
Hn
Hl
M
message
M
Ht
M
Hn
frame
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
Ht
Hn
Hl
M
message
M
Ht
M
Hn
frame
network
link
physical

## Slide 5: Transport services and protocols
provide logical communication between app processes running on different hosts
transport protocols run in end systems
  send side: breaks app messages into segments, passes to network layer
  rcv side: reassembles segments into messages, passes to app layer
more than one transport protocol available to apps
  Internet: TCP and UDP
application
transport
network
data link
physical
logical end-end transport
application
transport
network
data link
physical

## Slide 6: Transport services and protocols
provide logical communication between app processes running on different hosts
transport protocols run in end systems, not at network core (e.g. network routers)
  send side: breaks app messages into smaller chunks and adds a transport-layer header to each chunk to create the transport-layer segments. The transport layer then passes the segment to the network layer, where the segment is encapsulated within a datagram (i.e., the network layer packet),
  receiving side: extract the segment from the datagram, reassembles segments into messages, and passes to app layer
Datagrams are routed through intermediate nodes (routers)
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
Ht
Hn
Hl
M
message
M
Ht
M
Hn
frame
Source
Destination
Encapsulation
Notes: By logical communication, from an application’s perspective, it is as if the hosts running the processes were directly connected. Application processes use the logical communication provided by the transport layer to send messages to each other, free from the worry of the details of the physical infrastructure used to carry these messages. transport-layer protocols are implemented in the end systems but not in network routers.
On the sending side, the transport layer converts
the application-layer messages it receives from a sending application process into transport-layer packets, known as transport-layer segments in Internet terminology. This is done by (possibly) breaking the application messages into smaller chunks and adding a transport-layer header to each chunk to create the transport-layer segment. The transport layer then passes the segment to the network layer at the sending end system, where the segment is encapsulated within a network-layer packet (a datagram) and sent to the destination. It’s important to note that network routers act only on the network-layer fields of the datagram; that is, they do not examine the fields of the transport-layer segment encapsulated with the datagram. On the receiving side, the network layer extracts the transport-layer segment from the datagram and passes the segment up to the transport layer. The transport layer then processes the received segment, making the data in the segment available to the receiving application.

## Slide 7: Transport vs. network layer
transport layer: provide logical communication between two processes running on different hosts
  Extends “host-to-host” communication to “process-to-process” communication
  Relies on, enhances, network layer services
  Segment
network layer: provide logical communication between two hosts
  Datagram
  Unreliable, best-effort delivery: Datagram’s may be lost, duplicated, reordered in the Internet – “best effort” service
12 kids in Ann’s house sending letters to 12 kids in Bill’s house:
hosts = houses
processes = kids
app messages = letters in envelopes
transport protocol = Ann and Bill who demux to in-house siblings
network-layer protocol = postal service
household analogy:
Notes: that the transport layer lies just above the network layer in the protocol stack. Whereas a transport-layer protocol provides logical communication between processes running on different hosts, a network-layer protocol provides logical communication between hosts. This distinction is subtle but important. Let’s examine this distinction with the aid of a household analogy.
Within an end system, a transport protocol moves messages from application processes to the network edge (that is, the network layer) and vice versa, but it doesn’t have any say about how the messages are moved within the network core. In fact, as illustrated in Figure 3.1, intermediate routers neither act on, nor recognize, any information that the transport layer may have added to the application messages.
In a similar manner, the services that a transport protocol can provide are often constrained by the service model of the underlying network-layer protocol. If the network-layer protocol cannot provide delay or bandwidth guarantees for transport layer segments sent between hosts, then the transport-layer protocol cannot provide delay or bandwidth guarantees for application messages sent between processes.
Nevertheless, certain services can be offered by a transport protocol even when the underlying network protocol doesn’t offer the corresponding service at the network layer. For example, as we’ll see in this chapter, a transport protocol can offer reliable data transfer service to an application even when the underlying network protocol is unreliable, that is, even when the network protocol loses, garbles, or duplicates packets. As another example (which we’ll explore in Chapter 8 when we discuss network security), a transport protocol can use encryption to guarantee that application messages are not read by intruders, even when the network layer cannot guarantee the confidentiality of transport-layer segments.

## Slide 8: Transport vs. Network Layer service
Network layer: IP (Internet protocol) is the name of Internet’s network-layer protocol.
  IP provides unreliable, best-effort delivery
    No guarantees for delay, bandwidth, successful delivery, orderly delivery, or the integrity of the data.
Transport layer: Two transport layer protocols provide different services (not available: delay guarantees, bandwidth guarantees)
  TCP (Transmission Control Protocol) provides reliable, in-order delivery
    connection setup
    flow control, sequence numbers, acknowledgements, timers, error checking
    congestion control
  UDP (User Datagram Protocol) provides unreliable, unordered delivery
    error checking: providing integrity checking by including error-detection field in the segments’ headers
Notes: UDP (User Datagram Protocol) . TCP (Transmission Control Protocol)
UDP and TCP also provide integrity checking by including error detection fields in their segments’ headers. These two minimal transport-layer services— process-to-process data delivery and error checking—are the only two services that UDP provides
Both TCP and UDP packets as segments, and reserve the term datagram for the network-layer packet.
The Internet’s network-layer protocol has a name—IP, for Internet Protocol. IP provides logical communication between hosts. The IP service model is a best-effort delivery service. This means that IP makes its “best effort” to deliver segments between communicating hosts, but it makes no guarantees. In particular, it does not guarantee segment delivery, it does not guarantee orderly delivery of segments, and it does not guarantee the integrity of the data in the segments. For these reasons, IP is said to be an unreliable service. We also mention here that every host has at least one network-layer address, a so-called IP address.

## Slide 9: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 10: Multiplexing/demultiplexing
  use header info to deliver
  received transport layer
  segments to correct
  socket
demultiplexing at receiver:
  the job of gathering outgoing data chunk from different sockets at the source side, encapsulating each data chunk with header information to create segments, and passing the segments down to the network layer
multiplexing at sender:
process
socket
transport
application
physical
link
network
P2
P1
transport
application
physical
link
network
P4
transport
application
physical
link
network
P3
Extending host-to-host delivery to process-to-process delivery is called transport-layer multiplexing and demultiplexing.
Notes: At the destination host, the transport layer receives segments from the network layer just below. The transport layer has the responsibility of delivering the data in these segments to the appropriate application process running in the host. When the transport layer in your computer receives data from the network layer below, it needs to direct the received data to one of these four processes.
a process (as part of a network application) can have one or more sockets, doors through which data passes from the network to the
process and through which data passes from the process to the network. Thus, as shown in Figure 3.2, the transport layer in the receiving host does not actually deliver data directly to a process, but instead to an intermediary socket. Because at any given time there can be more than one socket in the receiving host, each socket has a unique identifier. The format of the identifier depends on whether the socket is a UDP or a TCP socket, as we’ll discuss shortly.
The job of gathering data chunks at the source host from different sockets, encapsulating each data chunk with header information (that will later be used in demultiplexing) to create segments, and passing the segments to the network layer is called multiplexing.
Each transport-layer segment has a set of fields in the segment for this purpose. At the receiving end, the transport layer examines these fields to identify the receiving socket and then directs the segment to that socket. This job of delivering the data in a transport-layer segment to the correct socket is called demultiplexing.
Note that the transport layer in the middle host in Figure 3.2 must demultiplex segments arriving from the network layer below to either
process P1 or P2 above; this is done by directing the arriving segment’s data to the corresponding process’s socket. The transport layer in the middle host must also gather outgoing data from these sockets, form transport-layer segments, and pass these segments down to the network layer.

## Slide 11: Multiplexing/demultiplexing
Socket
  Act as door, through which data passes from the network to the process and from process to the network. A host can have one or more sockets.
  A host has a unique IP address (32-bit for IPV4)
  Each socket has a port number (16-bit) at a host , ranging from 0 to 65535. The port numbers ranging from 0 to 1023 are called well-known port numbers and are restricted, which are reserved for use by well-known application protocols such as HTTP (port number 80) and FTP (port number 21).
process
socket
transport
application
physical
link
network
P2
P1
transport
application
physical
link
network
P4
transport
application
physical
link
network
P3
Notes: When a UDP socket is created in this manner, the transport layer automatically assigns a port number to the socket.
the client side of the application lets the transport layer automatically (and transparently) assign the port number, whereas the server side of the application assigns a specific port number.

## Slide 12: How demultiplexing works
host receives IP datagrams
  each datagram has source IP address, destination IP address
  each datagram carries one transport-layer segment
  each segment has source, destination port number
host uses IP addresses & port numbers to direct segment to appropriate socket
source port #
dest port #
32 bits
application
data
(payload)
other header fields
TCP/UDP segment format
Notes: transport-layer multiplexing requires (1) that sockets have unique identifiers, and (2) that each segment have special fields that indicate the socket to which the segment is to be delivered. These special fields, illustrated in Figure 3.3, are the source port number field and the destination port number field.

## Slide 13: Connectionless Mux/Demux (UDP)
An application program (i.e., Skype) creates a UDP socket in Host A
The transport layer in Host A does the UDP multiplexing (create segments, pass them to the network layer)
The network layer encapsulates the segment in an IP datagram and makes a best-effort delivery to the receiving host.
When receiving host gets UDP segment:
  checks destination port number in segment
  directs UDP segment to socket with that port number
Host uses both the dest. IP address and dest. Port number to direct segments to appropriate socket.
UDP socket is identified by two-tuple
  destination IP address
  destination port number

## Slide 14: Connectionless demux: example
DatagramSocket serverSocket = new DatagramSocket
(6428);
transport
application
physical
link
network
P3
transport
application
physical
link
network
P1
transport
application
physical
link
network
P4
DatagramSocket mySocket1 = new DatagramSocket (5775);
DatagramSocket mySocket2 = new DatagramSocket
(9157);
source port: 9157
dest port: 6428
source port: 6428
dest port: 9157
source port: ?
dest port: ?
source port: ?
dest port: ?
if two UDP segments have different source IP addresses and/or source port numbers, but have the same destination IP address and destination port number, then the two segments will be directed to the same destination process via the same destination socket.
Notes: Typically, the client side of the application lets the transport layer automatically (and transparently) assign the port number, whereas the server side of the application assigns a specific port number.
Suppose a process in Host A, with UDP port 19157, wants to send a chunk of application data to a process with UDP port 46428 in Host B. The transport layer in Host A creates a transport-layer segment that includes the application data, the source port number (19157), the destination port number (46428), and two other values (which will be discussed later, but are unimportant for the current discussion). The transport layer then passes the resulting segment to the network layer. The network layer encapsulates the segment in an IP datagram and makes a best-effort attempt to deliver the segment to the receiving host.
If the segment arrives at the receiving Host B, the transport layer at the receiving host examines the destination port number in the segment (46428) and delivers the segment to its socket identified by port 46428. Note that Host B could be running multiple processes, each with its own UDP socket and associated port number. As UDP segments arrive from the network, Host B directs (demultiplexes) each segment to the appropriate socket by examining the segment’s destination port number. Host B directs (demultiplexes) each segment to the appropriate socket by examining the segment’s destination port number. As a consequence, if two UDP segments have different source IP addresses and/or source port numbers, but have the same destination IP address and destination port number, then the two segments will be directed to the same destination process via the same destination socket.
in the A-to-B segment the source port number serves as part of a “return address”—when B wants to send a segment back to A, the destination port in the B-to-A segment will take its value from the source port value of the A-to-B segment.

## Slide 15: Connection-oriented demux
TCP socket identified by 4-tuple:
  source IP address
  source port number
  dest IP address
  dest port number
demux: receiver uses all four values to direct segment to appropriate socket
server host may support many simultaneous TCP sockets:
  each socket identified by its own 4-tuple
web servers have different sockets for each connecting client
  non-persistent HTTP will have different socket for each request
  Persistent HTTP will have the same server socket for exchanging messages
Notes: One subtle difference between a TCP socket and a UDP socket is that a TCP socket is identified by a four-tuple: (source IP address, source port number, destination IP address, destination port number). two arriving TCP segments with different source IP addresses or source port numbers will (with the exception of a TCP segment carrying the original connection-establishment request) be directed to two different sockets.
If the client and server are using persistent HTTP, then throughout the duration of the persistent connection the client and server exchange HTTP messages via the same server socket. However, if the client and server use non-persistent HTTP, then a new TCP connection is created and closed for every request/response, and hence a new socket is created and later closed for every request/response. This frequent
creating and closing of sockets can severely impact the performance of a busy Web server (although a number of operating system tricks can be used to mitigate the problem)

## Slide 16: Connection-oriented demux: example
transport
application
physical
link
network
P3
transport
application
physical
link
P4
transport
application
physical
link
network
P2
source IP,port: A,9157
dest IP, port: B,80
source IP,port: B,80
dest IP,port: A,9157
host: IP address A
host: IP address C
network
P6
P5
P3
source IP,port: C,5775
dest IP,port: B,80
source IP,port: C,9157
dest IP,port: B,80
Two clients, using the same destination port number (80) to
communicate with the same Web server application
server: IP address B
Two arriving TCP segments with different source IP addresses or source port numbers will be directed to two different sockets.
Per-connection http processes
Notes: The situation is illustrated in Figure 3.5, in which Host C initiates two HTTP sessions to server B, and Host Ainitiates one HTTP session to B. Hosts Aand C and server B each have their own unique IP address—A, C, and B, respectively. Host C assigns two different source port numbers (26145 and 7532) to its two HTTP connections. Because Host A is choosing source port numbers independently of C, it might also assign a source port of 26145 to its HTTP connection. But this is not a problem—server B will still be able to correctly demultiplex the two connections having the same source port number, since the two connections have different source IP addresses.
all subsequently arriving segments whose source port, source IP address, destination port, and destination IP address match these four values will be demultiplexed to this socket.

## Slide 17: Connection-oriented demux: example
transport
application
physical
link
network
P3
transport
application
physical
link
transport
application
physical
link
network
P2
source IP,port: A,9157
dest IP, port: B,80
source IP,port: B,80
dest IP,port: A,9157
host: IP address A
host: IP address C
server: IP address B
network
P3
source IP,port: C,5775
dest IP,port: B,80
source IP,port: C,9157
dest IP,port: B,80
P4
threaded server
Today’s high-performing Web servers often use only one process, and create a new thread with a new connection socket for each new client connection.
Notes: For such a server, at any given time there may be many connection sockets (with different identifiers) attached to the same process.

## Slide 18: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 19: UDP: User Datagram Protocol [RFC 768]
UDP only provides essential functions that transport protocol can do (i.e. multiplexing/demultiplexing and some error check).
“best effort” service, UDP segments may be:
  lost
  delivered out-of-order to app
connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others
UDP use:
  streaming multimedia apps (loss tolerant, rate sensitive)
  DNS
reliable transfer over UDP:
  add reliability at application layer
  application-specific error recovery!
Notes: DNS is an example of an application-layer protocol that typically uses UDP.
When the DNS application in a host wants to make a query, it constructs a DNS query message and passes the message to UDP. Without performing any handshaking with the UDP entity running on the destination end system, the host-side UDP adds header fields to the message and passes the resulting segment to the network layer. The network layer encapsulates the UDP segment into a datagram and sends the datagram to a name server. The DNS application at the querying host then waits for a reply to its query. If it doesn’t receive a reply (possibly because the underlying network lost the query or the reply), either it tries sending the query to another name server, or it informs the invoking application that it can’t get a reply.
it is possible for an application to have reliable data transfer when using UDP. This can be done if reliability is built into the application itself (for example, by adding acknowledgment and retransmission mechanisms, such as those we’ll study in the next section). But this is a nontrivial task that would keep an application developer busy debugging for

## Slide 20: UDP: segment header
source port #
dest port #
32 bits
application
data
(payload)
UDP segment format
length
checksum
length, in bytes of UDP segment, including header
no connection establishment (which can add delay)
simple: no connection state at sender, receiver
small header size
no congestion control: UDP can blast away as fast as desired
why is there a UDP?
  Checksum: used by the receiving host to check whether error have been introduced into the segment during the transmission
  8 bytes header
Notes: UDP takes messages from the application process, attaches source and destination port number fields for the multiplexing/demultiplexing service, adds two other small fields, and passes the resulting segment to the network layer. The network layer encapsulates the transport-layer segment into an IP datagram and then makes a best-effort attempt to deliver the segment to the receiving host.
The UDP header has only four fields, each consisting of two bytes. The length field specifies the number of bytes in the UDP segment (header plus data). An explicit length value is needed since the size of the data field may differ from one UDP segment to the next. The checksum is used by the receiving host to check whether errors have been introduced into the segment. In truth, the checksum is also calculated over a few of the fields in the IP header in addition to the UDP segment. But we ignore this detail in order to see the forest through the trees.
If the segment arrives at the receiving host, UDP uses the destination port number to deliver the segment’s data to the correct application process.
TCP uses a three-way handshake before it starts to transfer data. UDP just blasts away without any formal preliminaries.
TCP maintains connection state in the end systems. This connection state includes receive and send buffers, congestion-control parameters,
and sequence and acknowledgment number parameters.
TCP, on the other hand, has a congestion-control mechanism that throttles the transport-layer TCP sender when one or more links between the source and destination hosts become excessively congested. TCP will also continue to resend a segment until the receipt of the segment has been acknowledged by the destination, regardless of how long reliable delivery takes.

## Slide 21: UDP checksum
sender:
treat segment contents, including header fields, as sequence of 16-bit integers
checksum: addition (one’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless? More later ….
Goal: detect “errors” (e.g., flipped bits) in transmitted segment
Notes: The UDP checksum provides for error detection. That is, the checksum is used to determine whether bits within the UDP segment have been altered (for example, by noise in the links or while stored in a router) as it moved from source to destination.
UDP at the sender side performs the 1s complement of the sum of all the 16-bit words in the segment, with any overflow encountered during the sum being wrapped around. This result is put in the checksum field of the UDP segment.
At the receiver, all four 16-bit words are added, including the checksum. If no errors are introduced into the packet, then clearly the
sum at the receiver will be 1111111111111111. If one of the bits is a 0, then we know that errors have been introduced into the packet.
0000+ //checksum用0加上

## Slide 22: Internet checksum: example
1’s complement sum
example: add two 16-bit integers
1 1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
1 0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
wraparound
sum
checksum
1. Add the 16-bit values up. Each time a carry-out (17th bit) is produced, swing that bit around and add it back into the LSb (one's digit). This is somewhat erroneously referred to as "one's complement addition."
2. Once all the values are added in this manner, invert all the bits in the result. A binary value that has all the bits of another binary value inverted is called its "one's complement," or simply its "complement."
Notes: Kurose and Ross forgot to say anything about wrapping the carry and adding it to low order bit.
The 1s complement is obtained by converting all the 0s to 1s and converting all the 1s to 0s. Thus the 1s complement of the sum 01001010110
00010 is 1011010100111101, which becomes the checksum
1’s complement sum and 2’s complement sum
  1’s complement sum is done by summing the numbers and adding the carry to the result
  2’s complement sum is done by summing the numbers and discarding the carry.
What that means is: 1. Add the 16-bit values up. Each time a carry-out (17th bit) is produced, swing that bit around and add it back into the LSb (one's digit). This is somewhat erroneously referred to as "one's complement addition."
2. Once all the values are added in this manner, invert all the bits in the result. A binary value that has all the bits of another binary value inverted is called its "one's complement," or simply its "complement."

## Slide 23: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 24: Principles of Reliable Data Transfer
important in application, transport, and link layers
How to provide the reliable data transfer on the top of an unreliable end-to-end network layer
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (RDT)
Sending
Process
Receiving
Process
Reliable Data Delivery
Sending
Process
Receiving
Process
Unreliable Date Delivery
RDT protocol
(sending side)
RDT protocol
(receiving side)
Application Layer
Network Layer
Transport Layer
a. Provided service
b. Service implementation
Notes: With a reliable channel, no transferred databits are corrupted (flipped from 0 to 1, or vice versa) or lost, and all are delivered in the order in which they were sent. This is precisely the service model offered by TCP to the Internet applications that invoke it. It is the responsibility of a reliable data transfer protocol to implement this service abstraction. This task is made difficult by the fact that the layer below the reliable data transfer protocol may be unreliable.
TCP is a reliable data transfer protocol that is implemented on top of an unreliable (IP) end-to-end network layer. we can view this lower layer simply as an unreliable point-to-point channel.

## Slide 25: Three Types of Channels
we’ll incrementally develop sender, receiver sides of reliable data transfer protocol (rdt)
Perfect channel: underlying channel is perfectly reliable
  no bit errors
  no loss of packets
Channel with bit errors
  All packets are received in correct order
  Packets may be corrupted (i.e., bits may be flipped)
“Loosy” channel: underlying channel not only corrupts bits in packets but also loses packets
  Packets may be lost
  Packets may be corrupted
Notes: Although we consider only unidirectional data transfer, it is important to note that the sending and receiving sides of our protocol will nonetheless need to transmit packets in both directions.

## Slide 26: Data Transfer over a Perfect Channel
underlying channel perfectly reliable
  no bit errors
  no loss of packets
consider only unidirectional data transfer, but control info will flow on both directions!
  sender sends data into underlying channel
  receiver reads data from underlying channel
there is no need for the receiver side to provide any feedback to the sender since nothing can go wrong!
Notes: with a perfectly reliable channel there is no need for the receiver side to provide any feedback to the sender since nothing can go wrong! Note that we have also assumed that the receiver is able to receive data as fast as the sender happens to send data. Thus, there is no need for the receiver to ask the sender to slow down!

## Slide 27: Data Transfer over Channel with Bit Errors
Assumptions
  All packets are received in correct order
  Packets may be corrupted (i.e., bits may be flipped)
  Checksum to detect bit errors
How to recover from bit errors? Use ARQ (automatic repeat request) mechanism
  acknowledgements (ACKs): receiver explicitly tells sender that packet received correctly
  negative acknowledgements (NAKs): receiver explicitly tells sender that packet is received with errors
  sender retransmits packet on receipt of NAK
new mechanisms in rdt2.0 (beyond rdt1.0):
  error detection
  Feedback : control message from receivers to senders
  Retransmission
Notes: We’ll continue to assume for the moment that all transmitted packets are received (although their bits may be corrupted) in the order in which they were sent.
ACK and NAK, These control messages allow the receiver to let the sender know what has been received correctly, and what has been received in error and thus requires repeating.
Error detection. First, a mechanism is needed to allow the receiver to detect when bit errors have occurred. Recall from the previous section that UDP uses the Internet checksum field for exactly this purpose.
Receiver feedback. Since the sender and receiver are typically executing on different end systems, possibly separated by thousands of miles, the only way for the sender to learn of the receiver’s view of the world (in this case, whether or not a packet was received correctly) is for the receiver to provide explicit feedback to the sender. The positive (ACK) and negative (NAK) acknowledgment replies in the message-dictation scenario are examples of such feedback. Our rdt2.0 protocol will similarly send ACK and NAK packets back from the receiver to the sender. In principle, these packets need only be one bit long; for example, a 0 value could indicate a NAK and a value of 1 could indicate an ACK.
Retransmission. A packet that is received in error at the receiver will be retransmitted by the sender.

## Slide 28: ARQ (automatic repeat request)
PKT(0)
PKT(1)
PKT(0)
ACK
ACK
sender
receiver
Everything is good
PKT(0)
PKT(0)
PKT(1)
NAK
ACK
sender
receiver
Received NAK

## Slide 29: a fatal flaw!
what happens if ACK/NAK corrupted?
sender doesn't know what happened at receiver!
can’t just retransmit: possible duplicate
handling duplicates:
sender retransmits current pkt if ACK/NAK corrupted
sender adds sequence number to each pkt
receiver discards (doesn’t deliver up) duplicate pkt
stop and wait
sender sends one packet,
then waits for receiver
response
x
Notes: The more difficult question is how the protocol should recover from errors in ACK or NAK packets. The difficulty here is that if an ACK or NAK is corrupted, the sender has no way of knowing whether or not the receiver has correctly received the last piece of transmitted data.
A third approach is for the sender simply to resend the current data packet when it receives a garbled ACK or NAK packet. This approach, however, introduces duplicate packets into the sender-to-receiver channel.
Thus, the sender will not send a new piece of data until it is sure that the receiver has correctly received the current packet. Because of this behavior, protocols such as rdt2.0 are known as stop-and-wait protocols.
For this simple case of a stop-and wait protocol, a 1-bit sequence number will suffice, since it will allow the receiver to know whether the sender is resending the previously transmitted packet (the sequence number of the received packet has the same sequence number as the most recently received packet) or a new packet (the sequence number changes, moving “forward” in modulo-2 arithmetic) Since we are currently assuming a channel that does not lose packets, ACK and NAK packets do not themselves need to indicate the sequence number of the packet they are acknowledging. The sender knows that a received ACK or NAK packet (whether garbled or not) was generated in response to its most recently transmitted data packet.

## Slide 30: Handling Duplicate Packets
PKT(0)
PKT(0)
PKT(1)
ACK
ACK
sender
receiver
x
Receiver expects
a pkt with seq. # 1
Duplicate pkt.
The receiver doesn’t know whether the ACK or NAK it last sent was received correctly at the sender. Thus, it cannot know a priori whether an arriving packet contains new data or is a retransmission!
A simple solution is to add a new field to the data packet and have the sender number its data packets by putting a sequence number into this field.
The receiver need only check this sequence number to determine whether or not the received packet is a retransmission.
Notes: The fundamental difficulty with duplicate packets is that the receiver doesn’t know whether the ACK or NAK it last sent was received correctly at the sender. Thus, it cannot know a priori whether an arriving packet contains new data or is a retransmission!
A simple solution to this new problem (and one adopted in almost all existing data transfer protocols, including TCP) is to add a new field to the data packet and have the sender number its data packets by putting a sequence number into this field. The receiver then need only check this sequence number to determine whether or not the received packet is a retransmission.

## Slide 31: A NAK-free Method
using ACKs only
instead of NAK, receiver sends ACK for correctly received packet with the highest in-order sequence number
  receiver must explicitly include seq # of pkt being ACKed into ACK
The sender that receives two ACKs for the same packets (that is, the sender receives duplicate ACKs) knows that the receive did not correctly receive the packet following the packet that is being ACKed twice, then retransmit this packet.
sender
receiver
PKT(0)
ACK(0)
PKT(1)
PKT(2)
ACK(0)
PKT(1)
x
Duplicate ACK
Receiver expects
a pkt with seq. # 1
Receiver expects
a pkt with seq. # 1
Notes: We can accomplish the same effect as a NAK if, instead of sending a NAK, we send an ACK for the last correctly received packet. Asender that receives two ACKs for the same packet (that is, receives duplicate ACKs) knows that the receiver did not correctly receive the packet following the packet that is being ACKed twice.

## Slide 32: The case of “Lossy” Channels
Assumption: underlying channel not only corrupt bits in packets but also lose packets (data or ACKs)
  Packets may be corrupted
  Packets may be lost
How to identify the packet lost?
Method:
  Set a timer: sender waits “reasonable” amount of time for ACK (a Time-Out).
Notes: Two additional concerns must now be addressed by the protocol: how to detect packet loss and what to do when packet loss occurs. The use of checksumming, sequence numbers, ACK packets, and retransmissions—the techniques already developed in rdt2.2—will allow us to answer the latter concern. Handling the first concern will require adding a new protocol mechanism.
we’ll put the burden of detecting and recovering from lost packets on the sender.

## Slide 33: Examples
The sender transmits a data packet and either that packet, or the receiver’s ACK of that packet, gets lost. In either case, no reply is forthcoming at the sender from the receiver. If the sender is willing to wait long enough so that it is certain that a packet has been lost, it can simply retransmit the data packet.
Notes: the sender transmits a data packet and either that packet, or the receiver’s ACK of that packet, gets lost. In either case, no reply is forthcoming at the sender from the receiver. If the sender is willing to wait long enough so that it is certain that a packet has been lost, it can simply retransmit the data packet. You should convince yourself that this protocol does indeed work.

## Slide 34: The case of “Lossy” Channels
Approach used in the case of “lossy” channel
  Set a timer: sender waits “reasonable” amount of time for ACK (a Time-Out).
  Sender adds sequence number to each packet.
  Receiver must specify sequence # of packet being ACKed.
  Sender retransmits current packet if ACK/NAK is corrupted or lost.
  Receiver discards (doesn’t deliver up) duplicate packet.

## Slide 35: Examples
How to set the value of time out is a key issue!
Notes: But how long must the sender wait to be certain that something has been lost? The sender must clearly wait at least as long as a round-trip delay between the sender and receiver (which may include buffering at intermediate routers) plus whatever amount of time is needed to process a packet at the receiver. In many networks, this worst-case maximum delay is very difficult even to estimate, much less know with certainty. Moreover, the protocol should ideally recover from packet loss as soon as possible; waiting for a worst-case delay could mean a long wait until error recovery is initiated. The approach thus adopted in practice is for the sender to judiciously choose a time value such that packet loss is likely, although not guaranteed, to have happened. If an ACK is not received within this time, the packet is retransmitted. Note that if a packet experiences a particularly large delay, the sender may retransmit the packet even though neither the data packet nor its ACK have been lost. This introduces the possibility of duplicate data packets in the sender-to-receiver channel. Happily, protocol rdt2.2 already has enough functionality (that is, sequence numbers) to handle the case of duplicate packets.
From the sender’s viewpoint, retransmission is a panacea. The sender does not know whether a data packet was lost, an ACK was lost, or if the packet or ACK was simply overly delayed. In all cases, the action is the same: retransmit. Implementing a time-based retransmission mechanism requires a countdown timer that can interrupt the sender after a given amount of time has expired. The sender will thus need to be able to (1) start the timer each time a packet (either a first-time packet or a retransmission) is sent, (2) respond to a timer interrupt (taking appropriate actions), and (3) stop the timer.

## Slide 36: Performance of “stop and wait”
performance stinks
e.g.: 1 Gbps link, 15 ms prop. delay, 8000 bit packet:
  U sender: utilization – fraction of time sender is busy sending
  if RTT=30 msec, 1KByte pkt every 30 msec: 267kbps throuput over 1 Gbps link
network protocol limits use of physical resources!
Dtrans =
L
R
8000 bits
109 bits/sec
=
=
8 microsecs
Notes: To appreciate the performance impact of this stop-and-wait behavior, consider an idealized case of two hosts, one located on the West Coast of the United States and the other located on the East Coast, as shown in Figure 3.17. The speed-of-light round-trip propagation delay between these two end systems, RTT, is approximately 30 milliseconds. Suppose that they are connected by a channel with a transmission rate, R, of 1 Gbps (109 bits per second). With a packet size, L, of 1,000 bytes (8,000 bits) per packet, including both header fields and data, the time needed to actually transmit the packet into the 1 Gbps link is dtrans
Figure 3.18(a) shows that with our stop-and-wait protocol, if the sender begins sending the packet at t = 0, then at t = L/R = 8 microseconds, the last bit enters the channel at the sender side. The packet then makes its 15-msec cross-country journey, with the last bit of the packet emerging at the receiver at t = RTT/2 + L/R = 15.008 msec. Assuming for simplicity that ACK packets are extremely small (so that
we can ignore their transmission time) and that the receiver can send an ACK as soon as the last bit of a data packet is received, the ACK emerges back at the sender at t = RTT + L/R = 30.008 msec. At this point, the sender can now transmit the next message. Thus, in 30.008 msec, the sender was sending for only 0.008 msec. If we define the utilization of the sender (or the channel) as the fraction of time the sender is actually busy sending bits into the channel, the analysis in Figure 3.18(a) shows
that the stop-and-wait protocol has a rather dismal sender utilization, Usender, of That is, the sender was busy only 2.7 hundredths of one percent of the time!
Viewed another way, the sender was able to send only 1,000 bytes in 30.008 milliseconds, an effective throughput of only 267 kbps—even though a 1 Gbps link was available! Imagine the unhappy network manager who just paid a fortune for a gigabit
capacity link but manages to get a throughput of only 267 kilobits per second!
This is a graphic example of how network protocols can limit the capabilities provided by the underlying network hardware. Also, we have neglected lower-layer protocol-processing times at the sender and receiver, as well as the processing and queuing delays that would occur at any intermediate routers between the sender and receiver. Including these effects would serve only to further increase the delay and further accentuate the poor performance.

## Slide 37: stop-and-wait operation
first packet bit transmitted, t = 0
sender
receiver
RTT
last packet bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
Low efficiency, low utilization
Stop and Wait: sender sends one packet, then waits for receiver response

## Slide 38: Stop-and-Wait Protocol
Features
  It has a timer implementation
  It has bit error detection mechanism
  Timer should be set for each individual packet
  Only 1 packet is sent at a time
  No pipelining
  Sender window size is 1
  Receiver window size is 1
Advantage
  Simple
Disadvantage
  Efficiency and utilization are very low

## Slide 39: How to Address the Low Efficiency of Stop-and-Wait Protocol
Solution: the sender is allowed to send multiple packets without waiting for acknowledgements
Pipelining: sender allows multiple, “in-flight”, yet-to-be-acknowledged packets. Since these in-transit packets can be visualized as filling a pipeline, this technique is known as pipelining.
Two features of pipelined protocol
  The range of sequence numbers must be increased.
  The sender and the receiver may have to buffer more than one packet.
Notes: if the sender is allowed to transmit three packets before having to wait for acknowledgments, the utilization of the sender is essentially tripled. Since the many in-transit sender-to-receiver packets can be visualized as filling a pipeline, this technique is known as pipelining. Pipelining has the following consequences for reliable data transfer protocols:
The range of sequence numbers must be increased, since each in-transit packet (not counting retransmissions) must have a unique sequence number and there may be multiple, in-transit, unacknowledged packets.
• The sender and receiver sides of the protocols may have to buffer more than one packet. Minimally, the sender will have to buffer packets that have been transmitted but not yet acknowledged. Buffering of correctly received packets may also be needed at the receiver, as discussed below.
• The range of sequence numbers needed and the buffering requirements will depend on the manner in which a data transfer protocol responds to lost, corrupted, and overly delayed packets. Two basic approaches toward pipelined error recovery can be identified: Go-Back-N and selective repeat.

## Slide 40: Pipelined protocols
Two generic forms of pipelined protocols
  go-Back-N
  selective repeat

## Slide 41: Pipelining: increased utilization
first packet bit transmitted, t = 0
sender
receiver
RTT
last bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
last bit of 2nd packet arrives, send ACK
last bit of 3rd packet arrives, send ACK
3-packet pipelining increases
utilization by a factor of 3!

## Slide 42: Go-Back-N
A pipelined protocol
It improves the transmission efficiency
  It introduces a window of size N: N is called as window size.
It allows up to N unACKed packets in the network
  Sender can transmit N packets into the network before receiving an ACK
Concepts
  Window size
  Sequence number
  Cumulative acknowledgement
  How to deal with out-of-order packets
  Timer and timeout
http://media.pearsoncmg.com/aw/ecs_kurose_compnetwork_6/video_applets/GBNindex.html
Notes: In a Go-Back-N (GBN) protocol, the sender is allowed to transmit multiple packets (when available) without waiting for an acknowledgment, but is constrained to have no more than some maximum allowable number, N, of unacknowledged packets in the pipeline.

## Slide 43: GBN in action
0 1 2 3 4 5 6 7 8 9
Window size N (here N=4):
  Label each packet with a sequence number.
  A window is a collection of adjacent sequence numbers.
  The size of the collection is the sender’s window size.
  If window not full, transmit.
Notes: Sequence numbers in the interval [0,base-1] correspond to packets that have already been transmitted and acknowledged. The interval [base,nextseqnum-1] corresponds to packets that have been sent but not yet acknowledged. Sequence numbers in the interval [nextseqnum,base+N-1] can be used for packets that can be sent immediately, should data arrive from the upper layer.
the range of permissible sequence numbers for transmitted but not yet acknowledged packets can be viewed as a window of size N over the range of sequence numbers.
description of the sender and receiver sides of an ACK-based, NAK-free, GBN protocol.

## Slide 44: GBN in action
Cumulative acknowledgement: always send ACK for correctly-received packet with highest in-order seq #
  need only remember expected sequence number
  may generate duplicate ACKs
With cumulative acknowledge, an ACK indicates that all packets with a sequence number up to and including the number specified in the ACK have been correctly received.
Notes: Figure 3.22 shows the operation of the GBN protocol for the case of a window size of four packets. Because of this window size limitation, the sender sends packets 0 through 3 but then must wait for one or more of these packets to be acknowledged before proceeding. As each successive ACK (for example, ACK0 and ACK1) is received, the window slides forward and the sender can transmit one new packet (pkt4 and pkt5, respectively). On the receiver side, packet 2 is lost and thus packets 3, 4, and 5 are found to be out of order and are discarded.

## Slide 45: GBN in action
out-of-order packet:
  discard (don’t buffer) -> no receiver buffering!
  Re-ACK pkt with highest in-order seq #
0 1 2 3 4 5 6 7 8 9
0 1 2 3 4 5 6 7 8 9
0 1 2 3 4 5 6 7 8 9

## Slide 46: GBN in action
Timer and timeout:
  Uses a single timer – represents the oldest transmitted, but not yet ACKed pkt
  If an ACK is received but there are still other transmitted but not yet ACKed packets, the timer is restarted.
  On timeout, send all packets previously sent but not yet ACKed.
0 1 2 3 4 5 6 7 8 9
0 1 2 3 4 5 6 7 8 9
0 1 2 3 4 5 6 7 8 9
Notes: If a timeout occurs, the sender resends all packets that have been previously sent but that have not yet been acknowledged. Our sender in Figure 3.20 uses only a single timer, which can be thought of as a timer for the oldest transmitted but not yet acknowledged packet. If an ACK is received but there are still additional transmitted but not yet acknowledged packets, the timer is restarted. If there are no outstanding, unacknowledged packets, the timer is stopped.

## Slide 47: Go-Back-N
Sender Operation:
  Label each packet with a sequence number
  A window is a collection of adjacent sequence numbers
  The size of the collection is the sender’s window size
  If window not full, sender transmits packets
  ACKs are cumulative
  Timer and timeout
    On timeout, sender sends all packets previously sent but not yet ACKed.
    Uses a single timer – represents the oldest transmitted, but not yet ACKed packet.
Notes: flow control is one reason to impose a limit on the sender. In practice, a packet’s sequence number is carried in a fixed-length field in the packet header.
In our GBN protocol, an acknowledgment for a packet with sequence number n will be taken to be a cumulative acknowledgment, indicating that all packets with a sequence number up to and including n have been correctly received at the receiver.
A timeout event. The protocol’s name, “Go-Back-N,” is derived from the sender’s behavior in the presence of lost or overly delayed packets. As in the stop-and-wait protocol, a timer will again be used to recover from lost data or acknowledgment packets. If a timeout occurs, the sender resends all packets that have been previously sent but that have not yet been acknowledged. Our sender in Figure 3.20 uses only a single timer, which can be thought of as a timer for the oldest transmitted but
not yet acknowledged packet. If an ACK is received but there are still additional transmitted but not yet acknowledged packets, the timer is restarted. If there are no outstanding, unacknowledged packets, the timer is stopped.

## Slide 48: Go-Back-N
Receiver Operation:
  ACK-only: always send ACK for correctly-received pkt with highest in-order seq #
    may generate duplicate ACKs
    need only remember expectedseqnum
  out-of-order pkt:
    discard (don’t buffer): no receiver buffering! deal the out-of-order by simply discarding the out-of-order packets.
    re-ACK pkt with highest in-order seq #
Notes: The receiver’s actions in GBN are also simple. If a packet with sequence number n is received correctly and is in order (that is, the data last delivered to the upper layer came from a packet with sequence number n – 1), the receiver sends an ACK for packet n and delivers the data portion of the packet to the upper layer. In all other cases, the receiver discards the packet and resends an ACK for the most recently received in-order packet. Note that since packets are delivered one at a time to the
upper layer, if packet k has been received and delivered, then all packets with a sequence number lower than k have also been delivered. Thus, the use of cumulative acknowledgments is a natural choice for GBN.
The advantage of this approach is the simplicity of receiver buffering—the receiver need not buffer any out-of-order packets. Thus, while the sender must maintain the upper and lower bounds of its window and the position of nextseqnum within this window, the only piece of information the receiver need maintain is the sequence number of the next in-order packet.

## Slide 49: Go-Back-N
Advantages
  Sender can send multiple packets at a time
  Efficiency is high compared with stop-and-wait protocol
  We can configure the window size
Disadvantage
  Sender needs to store the last unAcked N packets
  Retransmission of many error-free packets following an erroneous packet.
  It is inefficient when round-trip delay large and data transmission rate is high.
Notes: In particular, when the window size and bandwidth-delay product are both large, many packets can be in the pipeline. A single packet error can thus cause GBN to retransmit a large number of packets, many unnecessarily. As the probability of channel errors increases, the pipeline can become filled with these unnecessary retransmissions.

## Slide 50: Selective repeat
It is proposed to overcome the unnecessarily retransmitting the error-free packets.
  having the sender retransmit only those packets that it suspects were received in error (that is, were lost or corrupted) at the receiver.
Concepts:
  Sender window size
  Sequence number
  Not cumulative acknowledgement
  How to deal with out-of-order packets
  Timer and timeout
http://media.pearsoncmg.com/aw/ecs_kurose_compnetwork_6/video_applets/SRindex.html
Notes: As the name suggests, selective-repeat protocols avoid unnecessary retransmissions by having the sender retransmit only those packets that it suspects were received in error (that is, were lost or corrupted) at the receiver. This individual, as needed, retransmission will require that the receiver individually acknowledge correctly received packets. A window size of N will again be used to limit the number

## Slide 51: Selective repeat
Window size N
  Data is received from above layer. Label each packet with a sequence number.
  if next available seq # in window, send pkt
ACK is not cumulative
  Receiver individually acknowledges all correctly received pkts (ACK is not cumulative)
  Mark packet n as received
  If n is the smallest unACKed pkt, advance window base to next unACKed packet with the smallest seq #. After moving window, if there are untransmitted packets with sequence numbers within the window, these packets are transmitted
How to deal with the out-of-order packets:
  Buffer is needed for eventual in-order delivery packets to upper layer
Timer and timeout
  Sender sets timer for each unACKed pkt (multiple timers)
  If packet n is timeout, resend pkt n and restart timer
Notes: selective-repeat protocols avoid unnecessary retransmissions by having the sender retransmit only those packets that it suspects were received in error (that is, were lost or corrupted) at the receiver. This individual, asneeded, retransmission will require that the receiver individually acknowledge correctly received packets.
A window size of N will again be used to limit the number of outstanding, unacknowledged packets in the pipeline. However, unlike GBN, the sender will have already received ACKs for some of the packets in the window.
The SR receiver will acknowledge a correctly received packet whether or not it is in order. Out-of-order packets are buffered until any missing packets (that is, packets with lower sequence numbers) are received, at which point a batch of packets can be delivered in order to the upper layer.

## Slide 52: Selective repeat: sender, receiver windows

## Slide 53: Selective repeat
data from above:
if next available seq # in window, send pkt
timeout(n):
resend pkt n, restart timer
ACK(n) in [sendbase,sendbase+N]:
mark pkt n as received
if n smallest unACKed pkt, advance window base to next unACKed seq #
sender
pkt n in [rcvbase, rcvbase+N-1]
send ACK(n)
out-of-order: buffer
in-order: deliver (also deliver buffered, in-order pkts), advance window to next not-yet-received pkt
pkt n in [rcvbase-N,rcvbase-1]
ACK(n)
otherwise:
ignore
receiver

## Slide 54: Selective Repeat Example: Window Size N=4
Notes: the receiver initially buffers packets 3, 4, and 5, and delivers them together with packet 2 to the upper layer when packet 2 is finally received.
the receiver reacknowledges (rather than ignores) already received packets with certain sequence numbers below the current window base. You should convince yourself that this reacknowledgmentis indeed needed.

## Slide 55: Selective repeat: dilemma
example:
seq #’s: 0, 1, 2, 3
window size=3
receiver window
(after receipt)
sender window
(after receipt)
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
timeout
retransmit pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
X
X
will accept packet
with seq number 0
(b) oops!
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
will accept packet
with seq number 0
0 1 2 3 0 1 2
pkt3
(a) no problem
receiver can’t see sender side.
receiver behavior identical in both cases!
something’s (very) wrong!
receiver sees no difference in two scenarios!
duplicate data accepted as new in (b)
Q: what relationship between seq # size and window size to avoid problem in (b)?
SR receiver dilemma with too-large windows: A new packet
or a retransmission?
Notes: Consider what could happen, for example, with a finite range of four packet sequence numbers, 0, 1, 2, 3, and a window size of three. Suppose packets 0 through 2 are transmitted and correctly received and acknowledged at the receiver. At this point, the receiver’s window is over the fourth, fifth, and sixth packets, which have sequence numbers 3, 0, and 1, respectively. Now consider two scenarios.
In the first scenario, shown in Figure 3.27(a), the ACKs for the first three packets are lost and the sender retransmits these packets. The receiver thus next receives a packet with sequence number 0—a copy of the first packet sent.
In the second scenario, shown in Figure 3.27(b), the ACKs for the first three packets are all delivered correctly. The sender thus moves its window forward and sends the fourth, fifth, and sixth packets, with sequence numbers 3, 0, and 1, respectively.
The packet with sequence number 3 is lost, but the packet with sequence number 0 arrives—a packet containing new data.
There is no way of distinguishing the retransmission of the first packet from an original transmission of the fifth packet. Clearly, a window size that is 1 less than the size of the sequence number space won’t work. But how small must the window size be? A problem at the end of the chapter asks you to show that the window size must be less than or equal to half the size of the sequence number space for SR protocols.

## Slide 56: Pipelined protocols: overview
Go-back-N:
sender can have up to N unacked packets in pipeline
receiver only sends cumulative ack
  doesn’t ack packet if there’s a gap
sender has timer for oldest unacked packet
  when timer expires, retransmit all unacked packets
Selective Repeat:
sender can have up to N unack’ed packets in pipeline
rcvr sends individual ack for each packet
sender maintains timer for each unacked packet
  when timer expires, retransmit only that unacked packet

## Slide 57: Comparison
Protocol | Stop and Wait | Go-Back-N | Selective Repeat
Bandwidth Utilization | Low | Medium | High
Maximum sender window size | 1 | the size of sequence number space | half of the size of the sequence number space
Maximum receiver window size | 1 | 1 | half of the size of the sequence number space
Pipelining | Not implemented | Implemented | Implemented
Out-of-order packets | Discarded | Discarded | Buffered
Cumulative ACK | N.A | Yes | No
Notes: But how small must the window size be? A problem at the end of the chapter asks you to show that the window size must be less than or equal to half the size of the sequence number space for SR protocols.

## Slide 58
Mechanism | 
Checksum | Used to detect bit errors in a transmitted packet.
Timer | Used to timeout/retransmit a packet, possibly because the packet (or its ACK) was lost within the channel.
Sequence number | Used for sequential numbering of packets of data flowing from sender to receiver. Gaps in the sequence numbers of received packets allow the receiver to detect a lost packet. Packets with duplicate sequence numbers allow the receiver to detect duplicate copies of a packet.
Acknowledgment | Used by the receiver to tell the sender that a packet or set of packets has been received correctly. Acknowledgments will typically carry the sequence number of the packet or packets being acknowledged. Acknowledgments may be individual or cumulative, depending on the protocol
Negative acknowledgment | Used by the receiver to tell the sender that a packet has not been received correctly. Negative acknowledgments will typically carry the sequence number of the packet that was not received correctly.
Window, pipelining | The sender may be restricted to sending only packets with sequence numbers that fall within a given range. By allowing multiple packets to be transmitted but not yet acknowledged, sender utilization can be increased over a stop-and-wait mode of operation.

## Slide 59: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 60: TCP: Overview RFCs: 793,1122,1323, 2018, 2581
full duplex data:
  bi-directional data flow in same connection
  MSS: maximum segment size (application layer data)
connection-oriented:
  TCP setup: three-way handshaking (exchange of control msgs) inits sender, receiver state before data exchange
  TCP teardown: close a TCP connection
point-to-point:
  one sender, one receiver
reliable, in-order byte steam:
pipelined:
  TCP congestion control
  TCP flow control
Send & receive bufferers
Notes: TCP is said to be connection-oriented because before one application process can begin to send data to another, the two processes must first “handshake” with each other—that is, they must send some preliminary segments to each other to establish the parameters of the ensuing data transfer. As part of TCP connection establishment, both sides of the connection will initialize many TCP state variables associated with the TCP connection.
TCP protocol runs only in the end systems and not in the intermediate network elements (routers and link-layer switches), the intermediate network elements do not maintain TCP connection state. In fact, the intermediate routers are completely oblivious to TCP connections; they see datagrams, not connections.
A TCP connection provides a full-duplex service: If there is a TCP connection between Process A on one host and Process B on another host, then application layer data can flow from Process A to Process B at the same time as application layer data flows from Process B to Process A. A TCP connection is also always point-to-point, that is, between a single sender and a single receiver. So-called “multicasting” (see Section 4.7)—the transfer of data from one sender to many receivers in a single send operation—is not possible with TCP.

## Slide 61: TCP segment structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
receive window
Urg data pointer
checksum
F
S
R
P
A
U
head
len
not
used
options (variable length)
URG: urgent data
(generally not used)
ACK: ACK #
valid
PSH: push data now
(generally not used)
RST, SYN, FIN:
connection estab
(setup, teardown
commands)
# the number of bytes
rcvr willing
to accept
counting
by bytes
of data
(not segments!)
Internet
checksum
(as in UDP)
the length of the typical TCP header is 20 bytes.)
MSS limits the maximum size of a segment’s application layer data field
Notes: TCP pairs each chunk of client data with a TCP header, thereby forming TCP segments. The TCP segment consists of header fields and a data field. The data field contains a chunk of application data. As mentioned above, the MSS limits the maximum size of a segment’s data field. When TCP sends a large file, such as an image as part of a Web page, it typically breaks the file into chunks of size MSS (except for the last chunk, which will often be less than the MSS).
As with UDP, the header includes source and destination port numbers, which are used for multiplexing/demultiplexing data from/to upper-layer applications. Also, as with UDP, the header includes a checksum field. A TCP segment header also contains the following fields:
The 32-bit sequence number field and the 32-bit acknowledgment number field are used by the TCP sender and receiver in implementing a reliable data transfer service, as discussed below.
• The 16-bit receive window field is used for flow control. We will see shortly that it is used to indicate the number of bytes that a receiver is willing to accept.
• The 4-bit header length field specifies the length of the TCP header in 32-bit words. The TCP header can be of variable length due to the TCP options field. (Typically, the options field is empty, so that the length of the typical TCP header is 20 bytes.)
• The optional and variable-length options field is used when a sender and receiver negotiate the maximum segment size (MSS) or as a window scaling factor for use in high-speed networks. A time-stamping option is also defined
• The flag field contains 6 bits. The ACK bit is used to indicate that the value carried in the acknowledgment field is valid; that is, the segment contains an acknowledgment for a segment that has been successfully received. The RST, SYN, and FIN bits are used for connection setup and teardown . Setting the PSH bit indicates that the receiver should pass the data to the upper layer immediately. Finally, the URG bit is used to indicate that there is data in this segment that the sending-side upper-layer entity has marked as “urgent.” The location of the last byte of this urgent data is indicated by the 16-bit urgent data pointer field. TCP must inform the receiving- side upper-layer entity when urgent data exists and pass it a pointer to the end of the urgent data. (In practice, the PSH, URG, and the urgent data pointer are not used. However, we mention these fields for completeness.)
The TCP payload size is calculated by taking the "Total Length" from the IP header (ip.len) and then substract the "IP header length" (ip.hdr_len) and the "TCP header length" (tcp.hdr_len).

## Slide 62: TCP Reliable Data Transfer
After a TCP connection is established, the two application processes can send data to each other.
Client app process passes a stream of data through the socket(the door of the process), then TCP running in the client handles these data (direct data to send buffer, break these data into chunks, pair each chunk of data with a TCP header to form a TCP segment, then pass them down to the network layer).

## Slide 63
Both the client and server allocate buffers to hold incoming and outgoing data to be transmitted or received throughput TCP protocol.
Sending buffer: buffer the outgoing data.
Receiving buffer: buffer the incoming data.
  The TCP does not know when the application will ask for any received data. TCP buffers incoming data so it is ready when the applications require them.
TCP Reliable Data Transfer

## Slide 64: How to Decide the Sequence No.
TCP views data as unstructured, but ordered stream of bytes.
We label these bytes with integer numbers.
Sequence number is the number of the first data in the segment in unit of bytes.
Sequence numbers are over bytes, not segments.
Example:
  The data file consisting of 500,000 bytes, MSS is 1000bytes, the initial sequence number is 0.
  TCP constructs 500 segments; the sequence number set in the first, second, third segments is 0, 1000, 2000, respectively.
Notes: Hexadecimal number system 十六进制

## Slide 65: How to Decide the ACK No.
Acknowledgement number – At host B(A), ACK number is the sequence number of the next byte that Host B(A) is expecting from host A(B).
Example:
  Host B received the 1st segment (i.e., all bytes numbered 0 through 999) from Host A and is waiting for all the subsequent segments.
  In this case, Host B puts 1000 in the ACK number field of the segment it sends to Host A.

## Slide 66: TCP seq. #’s and ACKs
Seq. #’s:
  byte stream “number” of first byte in segment’s data
ACKs:
  seq # of next byte expected from other side
  cumulative ACK
Q: how receiver handles out-of-order segments
  A: TCP spec doesn’t say, - up to implementer
Host A
Host B
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=43, ACK=80
User
types
‘C’
host ACKs
receipt
of echoed
‘C’
host ACKs
receipt of
‘C’, echoes
back ‘C’
time
simple telnet scenario

## Slide 67: Timer and Timeout
TCP uses single timer
Restart timer is triggered when
  A segment is sent and the timer is not running for any other segment.
  Timeout event happens.
  ACK is received.

## Slide 68: TCP round trip time, timeout
Q: how to set TCP timeout value?
longer than RTT
  but RTT varies
too short: premature timeout, unnecessary retransmissions
too long: slow reaction to segment loss, lead to large data transfer delay
Q: how to estimate RTT?
SampleRTT: measured time from segment transmission until ACK receipt
  ignore retransmissions
SampleRTT will vary, want estimated RTT “smoother”
  average several recent measurements, not just current SampleRTT
Notes: TCP, like our rdt protocol in Section 3.4, uses a timeout/retransmit mechanism to recover from lost segments. the most obvious question is the length of the timeout intervals. Clearly, the timeout should be larger than the connection’s round-trip time (RTT), that is, the time from when a segment is sent until it is acknowledged. Otherwise, unnecessary retransmissions would be sent.
The sample RTT, denoted SampleRTT, for a segment is the amount of time between when the segment is sent (that is, passed to IP) and when an acknowledgment for the segment is received.
Obviously, the SampleRTT values will fluctuate from segment to segment due to congestion in the routers and to the varying load on the end systems. Because of this fluctuation, any given SampleRTT value may be atypical. In order to estimate a typical RTT, it is therefore natural to take some sort of average of the SampleRTT values. TCP maintains an average, called EstimatedRTT, of the SampleRTT values. Upon obtaining a new SampleRTT, TCP updates EstimatedRTT according to the following formula:

## Slide 69: TCP round trip time, timeout
EstimatedRTT = (1- )*EstimatedRTT + *SampleRTT
exponential weighted moving average
influence of past sample decreases exponentially fast
typical value:  = 0.125
RTT (milliseconds)
RTT: gaia.cs.umass.edu to fantasia.eurecom.fr
sampleRTT
EstimatedRTT
time (seconds)

## Slide 70: TCP round trip time, timeout
timeout interval: EstimatedRTT plus “safety margin”
  large variation in EstimatedRTT -> larger safety margin
estimate SampleRTT deviation from EstimatedRTT:
DevRTT = (1-)*DevRTT +
*|SampleRTT-EstimatedRTT|
(typically,  = 0.25)
TimeoutInterval = EstimatedRTT + 4*DevRTT
estimated RTT
“safety margin”

## Slide 71: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 72: TCP reliable data transfer
TCP creates rdt service on top of IP’s unreliable service
  pipelined segments
  cumulative acks
  single retransmission timer
retransmissions triggered by:
  timeout events
  duplicate acks
Notes: Recall that the Internet’s network-layer service (IP service) is unreliable. IP does not guarantee datagram delivery, does not guarantee in-order delivery of datagrams, and does not guarantee the integrity of the data in the datagrams. With IP service, datagrams can overflow router buffers and never reach their destination, datagrams can arrive out of order, and bits in the datagram can get corrupted (flipped from 0 to 1 and vice versa). Because transport-layer segments are carried across the network by IP datagrams, transport-layer segments can suffer from these problems as well.
TCP creates a reliable data transfer service on top of IP’s unreliable besteffort service. TCP’s reliable data transfer service ensures that the data stream that a process reads out of its TCP receive buffer is uncorrupted, without gaps, without duplication, and in sequence; that is, the byte stream is exactly the same byte stream that was sent by the end system on the other side of the connection.
Thus, the recommended TCP timer management procedures [RFC 6298] use only a single retransmission timer, even if there are multiple transmitted but not yet acknowledged segments. The TCP protocol described in this section follows this single-timer recommendation.
Thus, the recommended TCP timer management procedures [RFC 6298] use only a single retransmission timer, even if there are multiple
transmitted but not yet acknowledged segments.

## Slide 73: TCP sender events:
data rcvd from app:
create segment with seq #
seq # is byte-stream number of first data byte in segment
start timer if not already running
  think of timer as for oldest unacked segment
  expiration interval: TimeOutInterval
timeout:
retransmit segment that caused timeout
restart timer
ack rcvd:
if ack acknowledges previously unacked segments
  update what is known to be ACKed
  start timer if there are still unacked segments
Three major events related to data transmission and retransmission in the TCP sender: data received from application above; timer timeout; and ACK receipt.
Notes: that there are three major events related to data transmission and retransmission in the TCP sender: data received from application above; timer timeout; and ACK receipt. Upon the occurrence of the first major event, TCP receives data from the application, encapsulates the data in a segment, and passes the segment to IP. Note that each segment includes a sequence number that is the byte-stream number of the first data byte in the segment, as described in Section 3.5.2. Also note that if the timer is already not running for some other segment, TCP starts the timer when the segment is passed to IP. (It is helpful to think of the timer as being associated with the oldest unacknowledged segment.) The expiration interval for this timer is the TimeoutInterval, which is calculated from EstimatedRTT and DevRTT, as described in Section 3.5.3.
The second major event is the timeout. TCP responds to the timeout event by retransmitting the segment that caused the timeout. TCP then restarts the timer.
The third major event that must be handled by the TCP sender is the arrival of an acknowledgment segment (ACK) from the receiver (more specifically, a segment containing a valid ACK field value). On the occurrence of this event, TCP compares the ACK value y with its variable SendBase. The TCP state variable SendBase is the sequence number of the oldest unacknowledged byte. (Thus SendBase–1 is the sequence number of the last byte that is known to have been received correctly and in order at the receiver.) As indicated earlier, TCP uses cumulative acknowledgments, so that y acknowledges the receipt of all bytes before byte number y. If y > SendBase, then the ACK is acknowledging one or more previously unacknowledged segments. Thus the sender updates its SendBase variable; it also restarts the timer if there currently are any not-yet-acknowledged segments.

## Slide 74: TCP: retransmission scenarios
lost ACK scenario
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
Seq=92, 8 bytes of data
X
timeout
ACK=100
premature timeout
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
Seq=92, 8
bytes of data
timeout
ACK=120
Seq=100, 20 bytes of data
ACK=120
SendBase=100
SendBase=120
SendBase=120
SendBase=92
Notes: Retransmission due to a lost acknowledgment. Host A sends one segment to Host B. Suppose that this segment has sequence number 92 and contains 8 bytes of data. After sending this segment, Host A waits for a segment from B with acknowledgment number 100. Although the segment from A is received at B, the acknowledgment from B to A gets lost. In this case, the timeout event occurs, and Host A retransmits the same segment. Of course, when Host B receives the retransmission, it observes from the sequence number that the segment contains data that has already been received. Thus, TCP in Host B will discard the bytes in the retransmitted segment.
Segment 100 not retransmitted. Host A sends two segments back to back. The first segment has sequence number 92 and 8 bytes of data, and the second segment has sequence number 100 and 20 bytes of data. Suppose that both segments arrive intact at B, and B sends two separate acknowledgments for each of these segments. The first of these acknowledgments has acknowledgment number 100; the second has acknowledgment number 120. Suppose now that neither of the acknowledgments arrives at Host A before the timeout. When the timeout event occurs, Host A resends the first segment with sequence number 92 and restarts the timer. As long as the ACK for the second segment arrives before the new timeout, the second segment will not be retransmitted.

## Slide 75: TCP: retransmission scenarios
X
cumulative ACK
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
Seq=120, 15 bytes of data
timeout
Seq=100, 20 bytes of data
ACK=120
Host A therefore knows that Host B has received everything up through byte 119; so Host A does not resend either of the two segments.
Notes: A cumulative acknowledgment avoids retransmission of the first segment. In a third and final scenario, suppose Host A sends the two segments, exactly as in the second example. The acknowledgment of the first segment is lost in the network, but just before the timeout event, Host A receives an acknowledgment with acknowledgment number 120. Host A therefore knows that Host B has received everything up through byte 119; so Host A does not resend either of the two segments.

## Slide 76: TCP fast retransmit
time-out period often relatively long:
  long delay before resending lost packet
detect lost segments via duplicate ACKs.
  sender often sends many segments back-to-back
  if segment is lost, there will likely be many duplicate ACKs.
if sender receives 3 ACKs for same data
(“triple duplicate ACKs”),
resend unacked segment with smallest seq #
  likely that unacked segment lost, so don’t wait for timeout
TCP fast retransmit
Notes: One of the problems with timeout-triggered retransmissions is that the timeout period can be relatively long. When a segment is lost, this long timeout period forces the sender to delay resending the lost packet, thereby increasing the end-to end delay. Fortunately, the sender can often detect packet loss well before the timeout event occurs by noting so-called duplicate ACKs. A duplicate ACK is an ACK that reacknowledges a segment for which the sender has already received an earlier acknowledgment.
Since TCP does not use negative acknowledgments, the receiver cannot send an explicit negative acknowledgment back to the sender. Instead, it simply reacknowledges (that is, generates a duplicate ACK for) the last in-order byte of data it has received.
Because a sender often sends a large number of segments back to back, if one segment is lost, there will likely be many back-to-back duplicate ACKs. If the TCP sender receives three duplicate ACKs for the same data, it takes this as an indication that the segment following the segment that has been ACKed three times has been lost.
In the case that three duplicate ACKs are received, the TCP sender performs a fast retransmit [RFC 5681], retransmitting the missing segment before that segment’s timer expires.

## Slide 77: TCP fast retransmit
X
fast retransmit after sender
receipt of triple duplicate ACK
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
timeout
ACK=100
ACK=100
ACK=100
Seq=100, 20 bytes of data
Seq=100, 20 bytes of data

## Slide 78: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 79: Buffers and Buffer Overflow
Both the client and server allocate buffers to hold incoming and outgoing data
Sending buffer:
  The application gives the TCP some data to send.
  The data is put in a sending buffer.
  The TCP won’t accept data from the application unless
  there is buffer space.
Receiving buffer
  When the TCP connection receives bytes that are correct and in sequence, it places the data in the receive buffer.
  The TCP does not know when the application will ask for the received data. TCP buffers incoming data so it is ready when the application ask for it.
Buffer overflow: the sender may easily overflow the receive buffer if the sender sends too much data too quickly and the application at the receiver is relatively slow at reading the data.
Notes: the hosts on each side of a TCP connection set aside a receive buffer for the connection. When the TCP connection receives bytes that are correct and in sequence, it places the data in the receive buffer. The associated application process will read data from this buffer, but not necessarily at the instant the data arrives.
Indeed, the receiving application may be busy with some other task and may not even attempt to read the data until long after it has arrived. If the application is relatively slow at reading the data, the sender can very easily overflow the connection’s receive buffer by sending too much data too quickly.

## Slide 80: TCP flow control
application
process
TCP socket
receiver buffers
TCP
code
IP
code
application
OS
receiver protocol stack
application may
remove data from
TCP socket buffers ….
… slower than TCP
receiver is delivering
(sender is sending)
from sender
receiver controls sender, so sender won’t overflow receiver’s buffer by transmitting too much, too fast
flow control
matching send rate to receiving application's drain rate
Speed Matching
Notes: TCP provides a flow-control service to its applications to eliminate the possibility of the sender overflowing the receiver’s buffer. Flow control is thus a speed-matching service—matching the rate at which the sender is sending against the rate at which the receiving application is reading. As noted earlier, a TCP sender can also be throttled due to congestion within the IP network; this form of sender control is referred to as congestion control.

## Slide 81: TCP flow control
buffered data
free buffer space
rwnd
RcvBuffer
TCP segment payloads
to application process
receiver “advertises” free buffer space by including rwnd value in TCP header of receiver-to-sender segments
  RcvBuffer size set via socket options (typical default is 4096 bytes)
  many operating systems autoadjust RcvBuffer
sender limits amount of unacked (“in-flight”) data to receiver’s rwnd value
guarantees receive buffer will not overflow
receiver-side buffering
unused buffer space:
= rwnd
= RcvBuffer-[LastByteRcvd -LastByteRead]

## Slide 82: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 83: How is a TCP Connection Established
An application process running in host A wants to initiate a connection with another application process running in host B
  The application process that initiates the connection is called client process, and the other application process is called server process.
  The client application process first informs the client transport layer that it wants to establish a connection to a process in the host B using a program command.
  Then, client transport layer proceeds to establish a TCP connection through three-way handshaking.
Socket clientSocket
= new Socket (“hostname”, “portNumber”)
Notes: Recall that the process that is initiating the connection is called the client process, while the other process is called the server process.

## Slide 84: Connection Management
before exchanging data, sender/receiver “handshake”:
agree to establish connection (each knowing the other willing to establish connection)
agree on connection parameters : seq.#s, buffers, flow control info (e.g. RcwWindow)
Client: connection initiator; Server: contacted by client.
connection state: ESTAB
connection variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
connection state: ESTAB
connection Variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
Socket clientSocket =
newSocket("hostname","port number");
Socket connectionSocket = welcomeSocket.accept();

## Slide 85: Three way handshaking
Step 1:client host sends TCP SYN segment to server
specifies initial seq #
no data
Step 2:server host receives SYN, replies with SYNACK segment
server allocates buffers
specifies server initial seq. #
Step 3:client receives SYNACK, replies with ACK segment, which may contain data
Notes: Step 1. The client-side TCP first sends a special TCP segment to the server-side TCP. This special segment contains no application-layer data. But one of the flag bits in the segment’s header (see Figure 3.29), the SYN bit, is set to 1. For this reason, this special segment is referred to as a SYN segment. In addition, the client randomly chooses an initial sequence number (client_isn) and puts this number in the sequence number field of the initial TCP SYN segment. This segment is encapsulated within an IP datagram and sent to the server. There has been considerable interest in properly randomizing the choice of the client_isn in order to avoid certain security attacks [CERT 2001–09].
Step 2. Once the IP datagram containing the TCP SYN segment arrives at the server host (assuming it does arrive!), the server extracts the TCP SYN segment from the datagram, allocates the TCP buffers and variables to the connection, and sends a connection-granted segment to the client TCP. This connection-granted segment also contains no applicationlayer data. However, it does contain three important pieces of information in the segment header. First, the SYN bit is set to 1. Second, the acknowledgment field of the TCP segment header is set to client_isn+1. Finally, the server chooses its own initial sequence number (server_isn) and puts this value in the sequence number field of the TCP segment header. This connection-granted segment is saying, in effect, “I received your SYN packet to start a connection with your initial sequence number, client_isn. I agree to establish this connection. My own initial sequence number is server_isn.” The connectiongranted segment is referred to as a SYNACK segment.
• Step 3. Upon receiving the SYNACK segment, the client also allocates buffers and variables to the connection. The client host then sends the server yet another segment; this last segment acknowledges the server’s connection-granted segment (the client does so by putting the value server_isn+1 in the acknowledgment field of the TCP segment header). The SYN bit is set to zero, since the connection is established. This third stage of the three-way handshake may carry client-to-server data in the segment payload.

## Slide 86: TCP 3-way handshake
SYNbit=1, Seq=x
choose init seq num, x
send TCP SYN msg
ESTAB
SYNbit=1, Seq=y
ACKbit=1; ACKnum=x+1
choose init seq num, y
send TCP SYNACK
msg, acking SYN
ACKbit=1, ACKnum=y+1
received SYNACK(x)
indicates server is live;
send ACK for SYNACK;
this segment may contain
client-to-server data
received ACK(y)
indicates client is live
SYNSENT
ESTAB
SYN RCVD
client state
LISTEN
server state
LISTEN
The first two segments carry no payload, that is, no application-layer data; the third of these segments may carry a payload.
Notes: Step 1. The client-side TCP first sends a special TCP segment to the server-side TCP. This special segment contains no application-layer data. But one of the flag bits in the segment’s header (see Figure 3.29), the SYN bit, is set to 1. For this reason, this special segment is referred to as a SYN segment. In addition, the client randomly chooses an initial sequence number (client_isn) and puts this number in the sequence number field of the initial TCP SYN segment. This segment is encapsulated within an IP datagram and sent to the server. There has been considerable interest in properly randomizing the choice of the client_isn in order to avoid certain security attacks [CERT 2001–09].
Step 2. Once the IP datagram containing the TCP SYN segment arrives at the server host (assuming it does arrive!), the server extracts the TCP SYN segment from the datagram, allocates the TCP buffers and variables to the connection, and sends a connection-granted segment to the client TCP. This connection-granted segment also contains no applicationlayer data. However, it does contain three important pieces of information in the segment header. First, the SYN bit is set to 1. Second, the acknowledgment field of the TCP segment header is set to client_isn+1. Finally, the server chooses its own initial sequence number (server_isn) and puts this value in the sequence number field of the TCP segment header. This connection-granted segment is saying, in effect, “I received your SYN packet to start a connection with your initial sequence number, client_isn. I agree to establish this connection. My own initial sequence number is server_isn.” The connectiongranted segment is referred to as a SYNACK segment.
• Step 3. Upon receiving the SYNACK segment, the client also allocates buffers and variables to the connection. The client host then sends the server yet another segment; this last segment acknowledges the server’s connection-granted segment (the client does so by putting the value server_isn+1 in the acknowledgment field of the TCP segment header). The SYN bit is set to zero, since the connection is established. This third stage of the three-way handshake may carry client-to-server data in the segment payload.

## Slide 87: TCP Connection Management (cont.)
Closing a connection:
client closes socket: clientSocket.close();
Step 1: client end system sends TCP FIN control segment to server
Step 2: server receives FIN, replies with ACK. Closes connection, sends FIN.
client
FIN
server
ACK
ACK
FIN
close
close
closed
timed wait
Note that the server could also choose to close the connection.
Notes: The client application process issues a close command. This causes the client TCP to send a special TCP segment to the server
process. This special segment has a flag bit in the segment’s header, the FIN bit (see Figure 3.29), set to 1. When the server receives this segment, it sends the client an acknowledgment segment in return. The server then sends its own shutdown segment, which has the FIN bit set to 1. Finally, the client acknowledges the server’s shutdown segment. At this point, all the resources in the two hosts are now deallocated.
Suppose that the client application decides it wants to close the connection. (Note that the server could also choose to close the connection.) This causes the client TCP to send a TCP segment with the FIN bit set to 1 and to enter the FIN_WAIT_1 state. While in the FIN_WAIT_1 state, the client TCP waits for a TCP segment from the server with an acknowledgment. When it receives this segment, the client TCP enters the FIN_WAIT_2 state. While in the FIN_WAIT_2 state, the client waits for another segment from the server with the FIN bit set to 1; after
receiving this segment, the client TCP acknowledges the server’s segment and enters the TIME_WAIT state. The TIME_WAIT state lets the TCP client resend the final acknowledgment in case the ACK is lost. The time spent in the TIME_WAIT state is implementation-dependent, but typical values are 30 seconds, 1 minute, and 2 minutes. After the wait, the connection formally closes and all resources on the client side (including port numbers) are released.

## Slide 88: TCP Connection Management (cont.)
Step 3: client receives FIN, replies with ACK.
  Enters “timed wait” - will respond with ACK to received FINs
Step 4: server, receives ACK. Connection closed.
Note: with small modification, can handle simultaneous FINs.
client
FIN
server
ACK
ACK
FIN
closing
closing
closed
timed wait
closed

## Slide 89: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 90: TCP congestion control: additive increase multiplicative decrease
approach: sender increases transmission rate (window size), probing for usable bandwidth, until loss occurs
  additive increase: increase cwnd by 1 MSS every RTT until loss detected
  multiplicative decrease: cut cwnd in half after loss
cwnd: TCP sender
congestion window size
AIMD saw tooth
behavior: probing
for bandwidth
additively increase window size …
…. until loss occurs (then cut window in half)
time
Notes: TCP’s congestion control consists of linear (additive) increase in cwnd of 1 MSS per RTT and then a halving (multiplicative decrease) of cwnd on a triple duplicate-ACK event. For this reason, TCP congestion control is often referred to as an additive-increase, multiplicativedecrease
(AIMD) form of congestion control. AIMD congestion control gives rise to the “saw tooth” behavior shown in Figure 3.54, which also nicely illustrates our earlier intuition of TCP “probing” for bandwidth—TCP linearly increases its congestion window size (and hence its transmission rate) until a triple duplicate-ACK event occurs. It then decreases its congestion window size by a factor of two but then again begins increasing it linearly, probing to see if there is additional available bandwidth.

## Slide 91: Congestion and TCP congestion control
congestion: informally: “too many sources sending too much data too fast for network to handle”
manifestations:
  lost packets (buffer overflow at routers)
  long delays (queueing in router buffers)
Mechanisms are needed to shrink the sending rate in the face of network congestion.
TCP congestion control mechanism
  How does a TCP sender limit the sending rate?
  How does a TCP sender perceive the degree of network congestion?
  What algorithm should the TCP sender use to adjust the sending rate?
Notes: Results in unfairness and poor utilization of network resources
  Resources are used by dropped packets (before they were lost)
  Retransmissions
  Poor resource allocation at high traffic load
The approach taken by TCP is to have each sender limit the rate at which it sends traffic into its connection as a function of perceived network congestion. If a TCP sender perceives that there is little congestion on the path between itself and the destination, then the TCP sender increases its send rate; if the sender perceives that there is congestion along the path, then the sender reduces its send rate. But this approach raises three questions. First, how does a TCP sender limit the rate at which it sends traffic into its connection? Second, how does a TCP sender perceive that there is congestion on the path between itself and the destination? And third, what algorithm should the sender use to change its send rate as a function of perceived end-to-end congestion?

## Slide 92: TCP Congestion Control
Congestion window (cwnd): a parameter to limit the transmission rate in sender
Sender limits transmission: the amount of unacknowledged data at a sender may not exceed the minimum of cwnd and rwnd
LastByteSent-LastByteAcked  min{CongWin, rwnd}
Roughly, sender’s send rate is
  At the beginning of every RTT, the constraint permits the sender to send cwnd bytes of data into the connection; at the end of the RTT the sender receives acknowledgments for the data.
CongWin is dynamic. It is a function of perceived network congestion.
rate =
CongWin
RTT
Bytes/sec
Notes: The TCP congestion-control mechanism operating at the sender keeps track of an additional variable, the congestion window. The congestion window, denoted cwnd, imposes a constraint on the rate at which a TCP sender can send traffic into the network. In order to focus on congestion control (as opposed to flow control), let us henceforth assume that the TCP receive buffer is so large that the receive-window constraint can be ignored; thus, the amount of unacknowledged data at the sender is solely limited by cwnd. We will also assume that the sender always has data to send, i.e., that all segments in the congestion window are sent.
The constraint above limits the amount of unacknowledged data at the sender and therefore indirectly limits the sender’s send rate. To see this, consider a connection for which loss and packet transmission delays are negligible. Then, roughly, at the beginning of every RTT, the constraint permits the sender to send cwnd bytes of data into the connection; at the end of the RTT the sender receives acknowledgments for the data. Thus the sender’s send rate is roughly cwnd/RTT bytes/sec. By adjusting the value of cwnd, the sender can therefore adjust the rate at which it sends data into its connection.

## Slide 93: TCP Congestion Control
How does sender perceive congestion:
  Loss event (a timeout or 3 duplicate ACKs)
TCP sender reduces rate (congestion window) after loss event.
TCP is self-clocking: TCP uses acknowledgements to trigger (clock) its adjustment of congestion window size
TCP congestion-control algorithm: three mechanisms
  Slow start (initial phase or after RTO (retransmission timeout)
  Additive-increase, multiplicative-decrease (AIMD)
  Reaction to timeout events: conservative after timeout event (CW=1 MSS (maximum segment size))
Notes: Let’s next consider how a TCP sender perceives that there is congestion on the path between itself and the destination. Let us define a “loss event” at a TCP sender as the occurrence of either a timeout or the receipt of three duplicate ACKs from the receiver. When there is excessive congestion, then one (or more) router buffers along the path overflows, causing a datagram (containing a TCP segment) to be dropped. The dropped datagram, in turn, results in a loss event at the sender—either a timeout or the receipt of three duplicate ACKs—which is taken by the sender to be an indication of congestion on the sender-to-receiver path.
when the network is congestion-free, that is, when a loss event doesn’t occur. In this case, acknowledgments for previously unacknowledged segments will be received at the TCP sender. As we’ll see, TCP will take the arrival of these acknowledgments as an indication that all is well—that segments being transmitted into the network are being successfully delivered to the destination—and will use acknowledgments to increase its congestion window size (and hence its transmission rate). Note that if acknowledgments arrive at a relatively slow rate (e.g., if the end-end path has high delay or contains a low-bandwidth link), then the congestion window will be increased at a relatively slow rate. On the other hand, if acknowledgments arrive at a high rate, then the congestion window will be increased more quickly. Because TCP uses acknowledgments to trigger (or clock) its increase in congestion window size, TCP is said to be self-clocking.
The algorithm has three major components: (1) slow start, (2) congestion avoidance, and (3) fast recovery. Slow start and congestion avoidance are mandatory components of TCP, differing
in how they increase the size of cwnd in response to received ACKs. We’ll see
shortly that slow start increases the size of cwnd more rapidly (despite its name!)
than congestion avoidance. Fast recovery is recommended, but not required, for
TCP senders.

## Slide 94: TCP congestion control: Slow Start
data segment
“Slow Start”: when connection begins, increase rate exponentially until first loss event
Initially: CW = 1 MSS
  example: MSS = 500 bytes & RTT = 200 msec
  initial rate = 20 kbps
increase rate exponentially until first loss event or when threshold reached
  double cwnd every RTT
  done by incrementing cwnd by 1 for every ACK received
CW  CW + 1
ACK
sender
cwnd
1
2
3
4
5
6
7
8
receiver
  double CongWin every RTT
  done by incrementing CongWin
  for every ACK received
http://histrory.visualland.net/tcp_swnd.html
Notes: When a TCP connection begins, the value of cwnd is typically initialized to a small value of 1 MSS [RFC 3390], resulting in an initial sending rate of roughly MSS/RTT. For example, if MSS = 500 bytes and RTT = 200 msec, the resulting initial sending rate is only about 20 kbps. Since the available bandwidth to the TCP sender may be much larger than MSS/RTT, the TCP sender would like to find the amount of available bandwidth quickly. Thus, in the slow-start state, the value of cwnd begins at 1 MSS and increases by 1 MSS every time a transmitted segment is first acknowledged. In the example of Figure 3.51, TCP sends the first segment into the network and waits for an acknowledgment. When this acknowledgment arrives, the TCP sender increases the congestion window by one MSS and sends out two maximum-sized segments. These segments are then acknowledged, with the sender increasing the congestion window by 1 MSS for each of the acknowledged segments, giving a congestion window of 4 MSS, and so on. This process results in a doubling of the sending rate every RTT. Thus, the TCP send rate starts slow but grows exponentially during the slow start phase.

## Slide 95: Transitioning into/out of slowstart
ssthresh: cwnd threshold maintained by TCP
on loss event: set ssthresh to cwnd/2
  Loss can be indicated by time out or 3 duplicated ACKs
  remember (half of) TCP rate when congestion last occurred
when cwnd >= ssthresh: transition from slowstart to congestion avoidance phase

## Slide 96: TCP: congestion avoidance
when cwnd > ssthresh grow cwnd linearly
  increase cwnd by 1 MSS per RTT
  approach possible congestion slower than in slowstart
  implementation: cwnd = cwnd + MSS/cwnd for each ACK received
ACKs: increase cwnd by 1 MSS per RTT: additive increase
loss: cut cwnd in half (non-timeout-detected loss ): multiplicative decrease
AIMD
AIMD: Additive Increase
Multiplicative Decrease
Notes: Thus, rather than doubling the value of cwnd every RTT, TCP adopts a more conservative approach and increases the value of cwnd by just a single MSS every RTT [RFC 2581]. This can be accomplished in several ways. A common approach is for the TCP sender to increase cwnd by MSS bytes (MSS/cwnd) whenever a new acknowledgment arrives. For example, if MSS is 1,460 bytes and cwnd is 14,600 bytes, then 10 segments are being sent within an RTT. Each arriving ACK (assuming one ACK per segment) increases the congestion window size by 1/10 MSS, and thus, the value of the congestion window will have increased by one MSS after ACKs when all 10 segments have been received.

## Slide 97: TCP: detecting, reacting to loss
Option 1: loss indicated by timeout:
  cwnd set to 1 MSS;
  window then grows exponentially (as in slow start) to threshold (, then grows linearly
Option 2: loss indicated by 3 duplicate ACKs: TCP RENO
  dup ACKs indicate network capable of delivering some segments
  cwnd is cut in half window then grows linearly
TCP Tahoe always sets cwnd to 1 (timeout or 3 duplicate acks)
11
13
12
14
15
17
16
11
10
X
11
11
10
11
Sender
Receiver
Notes: But when should this exponential growth end? Slow start provides several answers to this question. First, if there is a loss event (i.e., congestion) indicated by a timeout, the TCP sender sets the value of cwnd to 1 and begins the slow start process anew. It also sets the value of a second state variable, ssthresh (shorthand for “slow start threshold”) to cwnd/2—half of the value of the congestion window value when congestion was detected.
The second way in which slow start may end is directly tied to the value of ssthresh. Since ssthresh
is half the value of cwnd when congestion was last detected, it might be a bit reckless to keep doubling cwnd when it reaches or surpasses the value of ssthresh. Thus, when the value of cwnd equals ssthresh, slow start ends and TCP transitions into congestion avoidance mode. As we’ll see, TCP increases
In fast recovery, the value of cwnd is increased by 1 MSS for every duplicate ACK received for the missing segment that caused TCP to enter the fast-recovery state. Eventually, when an ACK arrives for the missing segment, TCP enters the congestion-avoidance state after deflating cwnd. If a timeout event occurs, fast recovery transitions to the slow-start state after performing the same actions as in slow start and congestion avoidance: The value of cwnd is set to 1 MSS, and the value of ssthresh is set to half the value of cwnd when the loss event occurred.
Fast recovery is a recommended, but not required, component of TCP [RFC 2581]. It is interesting that an early version of TCP, known as TCP Tahoe, unconditionally cut its congestion window to 1 MSS and entered the slow-start phase after either a timeout-indicated or triple-duplicate-ACK-indicated loss event. The newer version of TCP, TCP Reno, incorporated fast recovery.

## Slide 98: TCP: switching from slow start to CA
Q: when should the exponential increase switch to linear?
A: when cwnd gets to 1/2 of its value before timeout.
Implementation:
variable ssthresh
on loss event, ssthresh is set to 1/2 of cwnd just before loss event
the threshold is initially equal to 8 MSS.
Notes: Figure 3.53 illustrates the evolution of TCP’s congestion window for both Reno and Tahoe. In this figure, the threshold is initially equal to 8 MSS. For the first eight transmission rounds, Tahoe and Reno take identical actions. The congestion window climbs exponentially fast during slow start and hits the threshold at the fourth round of transmission. The congestion window then climbs linearly until a triple duplicate- ACK event occurs, just after transmission round 8. Note that the congestion window is 12 • MSS when this loss event occurs. The value of ssthresh is then set to 0.5 • cwnd = 6 • MSS. Under TCP Reno, the congestion window is set to cwnd = 6 • MSS and then grows linearly. Under TCP Tahoe, the congestion window is set to 1 MSS and grows exponentially until it reaches the value of ssthresh, at which point it grows linearly.
Figure 3.52 presents the complete FSM description of TCP’s congestioncontrol algorithms—slow start, congestion avoidance, and fast recovery. The figure also indicates where transmission of new segments or retransmitted segments can occur. Although it is important to distinguish between TCP error control/retransmission and TCP congestion control, it’s also important to appreciate how these two aspects of TCP are inextricably linked.

## Slide 99: Chapter 3: summary
principles behind transport layer services:
  multiplexing, demultiplexing
  reliable data transfer
  flow control
  congestion control
instantiation, implementation in the Internet
  UDP
  TCP
next:
leaving the network “edge” (application, transport layers)
into the network “core”