## Slide 1: DISCOVERING COMPUTERS 2018 Digital Technology, Data, and Devices
Module 8
Digital Storage: Preserving Content Locally and on the Cloud
Copyright © 2018 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 2: Objectives Overview (1 of 2)
Differentiate between storage and memory
Describe the characteristics of internal hard disks
Describe the benefits of solid-state drives
Identify uses of external hard drives and RAID
Differentiate among various types of memory cards and USB flash drives

## Slide 3: Objectives Overview (2 of 2)
Discuss the benefits and uses of cloud storage
Describe characteristics of and differentiate among types of optical discs
Explain types of enterprise storage
Identify uses of magnetic stripe cards, smart cards, RFID tags, and NFC tags

## Slide 4: Storage (1 of 10)
A storage medium is the physical material on which a computer keeps data, information, programs, and applications
Cloud storage keeps information on servers on the Internet, and the actual media on which the files are stored are transparent to the user

## Slide 5: Storage (2 of 10)
Figure 8-1 A variety of storage options.

## Slide 6: Storage (3 of 10)
A storage device is the hardware that records and/or retrieves items to and from storage media
Notes: Figure 2.1 Exercise/exercise dropout cycle

## Slide 7: Storage (4 of 10)
Capacity is the number of bytes a storage medium can hold
Table 8-1 Terms Used to Define Storage
Storage Term | Approximate Number of Bytes | Exact Number of Bytes
Kilobyte (KB) | 1 thousand | 210 or 1,024
Megabyte (MB) | 1 million | 210 or 1,048,576
Gigabyte (GB) | 1 billion | 230 or 1,073,741,824
Terabyte (TB) | 1 trillion | 240 or 1,099,511,627,776
Petabyte (PB) | 1 quadrillion | 250 or 1,125,899,906,842,624
Exabyte (EB) | 1 quintillion | 260 or 1,152,921,504,606,846,976
Zettabyte (ZB) | 1 sextillion | 270 or 1,180,591,620,717,411,303,424
Yottabyte (YB) | 1 septillion | 280 or 1,208,925,819,614,629,174,706,176

## Slide 8: Storage (5 of 10)
An Illustration of Volatility
State of Computer
Figure 8-2 A screen display is considered volatile because its contents disappear when power is removed. Likewise, most RAM is volatile. That is, its contents are erased when power is removed from a computer or mobile device. Storage, by contrast, is nonvolatile. Its contents remain when power is off.

## Slide 9: Storage (6 of 10)
Screen Display Volatile
Figure 8-2 A screen display is considered volatile because its contents disappear when power is removed. Likewise, most RAM is volatile. That is, its contents are erased when power is removed from a computer or mobile device. Storage, by contrast, is nonvolatile. Its contents remain when power is off.
Notes: Our environment is not conducive to a healthy, physically active lifestyle.

## Slide 10: Storage (7 of 10)
Contents of Most RAM Volatile
Figure 8-2 A screen display is considered volatile because its contents disappear when power is removed. Likewise, most RAM is volatile. That is, its contents are erased when power is removed from a computer or mobile device. Storage, by contrast, is nonvolatile. Its contents remain when power is off.

## Slide 11: Storage (8 of 10)
Contents of Storage Nonvolatile
Figure 8-2 A screen display is considered volatile because its contents disappear when power is removed. Likewise, most RAM is volatile. That is, its contents are erased when power is removed from a computer or mobile device. Storage, by contrast, is nonvolatile. Its contents remain when power is off.

## Slide 12: Storage (9 of 10)
Access time measures:
  The amount of time it takes a storage device to locate an item on a storage medium
  The time required to deliver an item from memory to the processor

## Slide 13: Storage (10 of 10)
Figure 8-3 A comparison of different types of storage media and memory in terms of relative speed and uses. Memory is faster than storage but is expensive and not practical for all storage requirements. Storage is less expensive but is slower than memory.

## Slide 14: Hard Drives (1 of 9)
Figure 8-4 The hard disk in a personal computer is enclosed inside an airtight, sealed case. In these photos of the desktop and laptop hard disks, the top plate is removed for illustration purposes. The laptop hard disk is much smaller than the desktop hard disk.
A hard disk, also called a hard disk drive (HDD) contains one or more inflexible, circular platters that use magnetic particles to store data, instructions, and information

## Slide 15: Hard Drives (2 of 9)
The storage capacity of hard disks varies and is determined by:
  The number of platters the hard disk contains
  The composition of the magnetic coating on the platters
  Whether the disk uses longitudinal or perpendicular recording
  Density

## Slide 16: Hard Drives (3 of 9)
Formatting is the process of dividing the disk into tracks and sectors
Figure 8-5 Tracks form circles on the surface of a hard disk. The disk’s storage locations are divided into wedge-shaped sections, which break the tracks into small arcs called sectors. Several sectors form a cluster.

## Slide 17: Hard Drives (4 of 9)
Characteristics of a hard disk include:
  Tracks
  Sectors
  Platters
  Form factor
  Read/write head
  Revolutions per minute

## Slide 18: Hard Drives (5 of 9)
Figure 8-6 This figure shows how a hard disk works.

## Slide 19: Hard Drives (6 of 9)
A head crash occurs when a read/write head touches the surface of a platter
Always keep a backup of your hard disk
Figure 8-7 The clearance between a hard disk read/write head and the platter is about two-millionths of an inch. Any contaminant could render the disk unusable.

## Slide 20: Hard Drives (7 of 9)
An SSD (solid state drive) is a flash memory storage device that contains its own processor to manage its storage
An SSD (solid state drive) has several advantages over traditional (magnetic) hard disks:
  Faster access times
  Faster transfer rates
  Quieter operation
  More durable
  Lighter weight
  Less power consumption
  Less heat generation
  Longer life
  Defragmentation not required

## Slide 21: Hard Drives (8 of 9)
An external hard drive is a separate freestanding storage device that connects with a cable to a USB port or other port on a computer or mobile device
Figure 8-9 Examples of external hard drives.

## Slide 22: Hard Drives (9 of 9)
RAID (redundant array of independent disks) is a group of two or more integrated hard drives
Figure 8-10 An example of RAID for the home or small business user.

## Slide 23: Portable Flash Memory Storage (1 of 5)
A memory card is a removable flash memory storage device that you insert and remove from a slot in a computer, mobile device, or card reader/writer
  SDHC
  SDXC
  miniSD
  microSDHC

## Slide 24: Portable Flash Memory Storage (2 of 5)
  microSDXC
  CF
  xD Picture Card
  Memory Stick PRO Duo
  M2

## Slide 25: Portable Flash Memory Storage (3 of 5)
Figure 8-11 Many types of computers and devices have slots for memory cards.

## Slide 26: Portable Flash Memory Storage (4 of 5)
Figure 8-12 This figure shows how an SD card works.

## Slide 27: Portable Flash Memory Storage (5 of 5)
USB flash drives plug into a USB port on a computer or mobile device
Figure 8-13 A close-up of the flash memory and circuitry inside a USB flash drive.

## Slide 28: Cloud Storage
Cloud storage is an Internet service that provides storage to computer or mobile device users

## Slide 29: Optical Discs (1 of 5)
An optical disc consists of a flat, round, portable disc made of metal, plastic, and lacquer that is written and read by a laser
Figure 8-14 An optical disc in a disc drive.

## Slide 30: Optical Discs (2 of 5)
How a Laser Reads Data on an Optical Disc
Figure 8-15 This figure shows how a laser reads data on an optical disc.

## Slide 31: Optical Discs (3 of 5)
Optical discs commonly store items in a single track that spirals from the center of the disc to the edge of the disc
Track is divided into evenly sized sectors
Figure 8-16 An optical disc typically stores data, instructions, and information in a single track that spirals from the center of the disc to the edge of the disc.

## Slide 32: Optical Discs (4 of 5)
A CD-ROM can be read from but not written to
  Single-session disc
A CD-R is an optical disc on which users can write once, but not erase
A CD-RW is an erasable multisession disc

## Slide 33: Optical Discs (5 of 5)
A DVD-ROM is a high-capacity optical disc on which users can read but not write on or erase
A DVD-R or DVD+R are competing DVD-recordable WORM formats, on which users can write once but not erase
DVD-RW, DVD+RW, and DVD+RAM are competing DVD-rewritable formats that users can write on multiple times

## Slide 34: Enterprise Storage (1 of 7)
Enterprise hardware allows large organizations to manage and store data and information using devices intended for heavy use, maximum efficiency, and maximum availability
  RAID duplicates data, instructions, and information to improve data reliability

## Slide 35: Enterprise Storage (2 of 7)
Figure 8-18 In RAID level 1, called mirroring, a backup disk exists for each drive. Other RAID levels use striping; that is, portions of each drive are placed on multiple drives.

## Slide 36: Enterprise Storage (3 of 7)
Network attached storage (NAS) is a server that is placed on a network with the sole purpose of providing storage to users, computers, and devices attached to the network

## Slide 37: Enterprise Storage (4 of 7)
Figure 8-19 An example of how network attached storage connects on a network.

## Slide 38: Enterprise Storage (5 of 7)
A storage area network (SAN) is a high-speed network with the sole purpose of providing storage to other attached servers
Figure 8-20 A storage area network provides centralized storage for servers and networks.

## Slide 39: Enterprise Storage (6 of 7)
Tape is a magnetically coated ribbon of plastic capable of storing large amounts of data and information
A tape drive reads and writes data and information on a magnetic tape

## Slide 40: Enterprise Storage (7 of 7)
Figure 8-21 A tape robot retrieves tape cartridges.

## Slide 41: Other Types of Storage (1 of 7)
A magnetic stripe card has a magnetic stripe that contains information
A smart card stores data on an integrated circuit embedded in the card

## Slide 42: Other Types of Storage (2 of 7)
Figure 8-22 The magnetic stripe on the back of credit cards and other ID cards contain information that identifies you and the card.

## Slide 43: Other Types of Storage (3 of 7)
Figure 8-23 Examples of contact and contactless smart cards and their readers.

## Slide 44: Other Types of Storage (4 of 7)
The RFID tag consists of an antenna and a memory chip that contains the information to be transmitted via radio waves
An RFID reader reads the radio signal and transfers the information to a computer or computing device

## Slide 45: Other Types of Storage (5 of 7)
Figure 8-24 An RFID reader reads radio signals from an RFID tag that is affixed to this box.

## Slide 46: Other Types of Storage (6 of 7)
An NFC-enabled device contains an NFC chip
An NFC tag contains a chip and an antenna that contains information to be transmitted
Most NFC tags are self-adhesive

## Slide 47: Other Types of Storage (7 of 7)
Figure 8-25 This NFC-enabled phone communicates with the NFC reader to send a mobile payment.

## Slide 48: Summary
Variety of storage options
Storage capacity and storage access times
Characteristics of hard disks, SSDs, external hard drives, and RAID
Portable flash memory storage
Advantages and various uses of cloud storage
Characteristics of optical discs
Enterprise storage options
Magnetic stripe cards, smart cards, RFID tags, and NFC chips and tags